## Slide 1: FIR Filter Design
Chapter 5
References:
J. H. McClellan, R. W. Schafer and M. A. Yoder, Signal Processing First, Pearson Education, Inc. 2003, Chapter 5 and 6.
S. K. Mitra, Digital Signal Processing – A Computer-Based Approach, McGraw-Hill International Edition, 4th Ed., 2011, Chapter 8 and 10.

## Slide 2: 5.1 What are digital filters?
In general, a filter is a system that removes the unwanted components in our input
In the context of DSP, a digital filter is a discrete-time system that removes the unwanted components in the input signal
Here, we are particularly interested in the digital filters that will remove the unwanted frequencies in the input signal
Can be further classified as
Low-pass
High-pass
Band-pass

## Slide 3: FIR Filters
If the impulse response of an LTI system is of a finite duration, the system is said to be a finite impulse response (FIR) system
If an FIR system is used for filtering purpose, it is called an FIR filter
An FIR filter is characterized by linear convolution in time domain
where N is the filter length and h is its impulse response and can be described in z-domain as

## Slide 4: Order and Taps
The above FIR filter is said to have an order of
It is based on the structure of a tapped delay line with taps
Z-1
Z-1
+
+
]
Z-1
+

## Slide 5: Characteristics of FIR filters
Stable – The behavior of an FIR filter usually will not change much due to the imperfection in the implementation
Linear phase response – An FIR filter can be easily designed to have the linear phase characteristics. Hence minimum distortion
Hardware cost – The hardware cost of an FIR filter is linearly proportional to the order of the filter (i.e. number of taps). One more tap  one more set of delay element, multiplier and adder
Delay – Input data need to go thru all the taps of an FIR filter before the output is obtained, which introduces system delay. Again, the amount of system delay is linearly proportional to the order of the filter, i.e. one more tap  one more clock cycle delay

## Slide 6: Design stages for FIR filters
Start
Obtain performance specifications
Calculate filter coefficients
Simulate with FIR structure
Finite wordlength effects analysis
Actual hardware/software implementation + testing
Stop
Re-design
Re-specify
Re-calculate
Re-structure

## Slide 7: FIR filter specifications
(in dB)
(in dB)
20log(1+p)
20log(s)

## Slide 8: Design method - Windowing
Design objective: obtain values of h[n] such that the resulting FIR filter meets the design specifications
  Magnitude response
  Linear phase property, etc.
For the windowing design method, we start with the ideal magnitude response HD(). Its impulse response hD[n] can be obtained by the inverse Fourier transform

## Slide 9: Window method
For instance, if a low pass filter is to be designed, we consider its ideal magnitude response
  
  
hD[n]
n
(time)
(frequency)
1

## Slide 10: Window method (cont)
The ideal impulse response is given by:
Unfortunately, the above ideal impulse response cannot be implemented by an FIR filter since it goes to infinite
An obvious solution is to truncate hD[n] by

## Slide 11: Frequency response of the truncated impulse response
Does the truncated impulse response have the ideal frequency response HD()? See the following example:
 Ts
Small M  big ripple, long transition width
Large M  the ripple becomes smaller when far away from the cutoff frequency, but becomes large when close to it (Gibb’s phenomenon), short transition width

## Slide 12: Ripples in the magnitude response
No matter how large M is (as long as it is finite), the truncation will always introduce ripples into the magnitude response
It can be explained as follows:
  Truncation is just equivalent to multiplying a rectangular window w to hD[n]: Let

## Slide 13: Ripples in the magnitude response (cont)
Convolution integral in frequency domain

## Slide 14: Truncation of ideal low pass filter
Rectangular
*
=
Frequency Domain
Time Domain
=
1

## Slide 15: Ripples in the magnitude response (cont)
Assume W () is a unit impulse at 0. The convolution of HD() and W () is just HD()
p
-p
0

1
p
-p
0

1

## Slide 16: Ripples in the magnitude response (cont)
But W () is not a unit impulse but a sinc function. The convolution of HD() and W() is not HD()
The ripples in the sinc function lead to the ripples in the final magnitude response
p
-p
0


## Slide 17: Convolution Integral
http://lpsa.swarthmore.edu/Convolution/ConvolveGUI.html

## Slide 19: To eliminate ripples …
It is now clear that ripples come from the spectral response of the window function
The closer W () is to a unit impulse, the closer HT() is to the ideal HD()
Can we design a window function with its spectrum response without ripples?
Yes, it depends on the shape of the window function in the time domain

## Slide 20: To eliminate ripple … (cont)
Rectangular
*
=
Frequency Domain
Time Domain
=
1

## Slide 21: To eliminate ripple … (cont)
*
=
Frequency Domain
Time Domain
=
Hamming

## Slide 22: Popular windows
The Triangular window
The Hamming window
The Blackman window

## Slide 23: Popular windows (cont)
The envelopes of various digital windows
Frequency Spectrum
Rectangular
Hamming
Triangular
Blackman
wi(n)
1
-1
0
Ts
0
Rectangular
Hamming
Triangular
Blackman
-

Hamming, Blackman and Triangular windows have no or very small ripples in their spectrum

## Slide 24: Popular windows (cont)
The magnitude response of an ideal low-pass digital filter truncated by using various windows with M = 5
Rectangular
Hamming
Triangular
Blackman
Ts
0
1
Hamming window gives the narrowest transition band (or smallest smearing or leakage)
Prefer in general applications
Note the passband frequency of HD() is at the middle of the transition band

## Slide 25: Determine the filter order
The transition width of a digital filter is closely related to the filter order
A higher filter order (longer length) is required for a sharp transition
Different window has different relationship between transition width and filter length
E.g., rectangular window:
where F is the transition width which is defined as F = fp - fs
fp = normalized frequency of the passband edge
fs = normalized frequency of the stopband edge

## Slide 26: Recall filter specifications
f
fs
fp
0
0.5
1
1-p
1+p
s
|HT(f)|
F
Passband
Stopband
Transition band
p = passband deviation (e.g. ≤ 0.01, i.e. 20log(1+0.01) ≈ 0.1 dB )
s = stopband deviation (e.g. ≤ 0.001, i.e. 20log(0+0.001) = -60 dB )
fp = passband edge frequency (e.g. 1600/8000 = 0.2, Fs = 8000)
fs = stopband edge frequency = (e.g. 2240/8000 = 0.28, Fs = 8000)
F = Transition Width = (fs – fp) (e.g. 0.28-0.2 = 0.08)
Stopband Attenuation
= -20log(s/(1- p)
≈ -20log(s)

## Slide 27: Important properties for windows
Window name | Transition width (normalized) | Passband ripple (dB) | Stopband attenuation (dB)
Rectangular | 0.9/2M | 0.7416 | 21
Hanning | 3.1/2M | 0.0546 | 44
Hamming | 3.3/2M | 0.0194 | 53
Blackman | 5.5/2M | 0.0017 | 75

## Slide 28: Design procedure
Specify the desired ideal frequency response, HD(ω)
Obtain the impulse response, hD[n], of the desired filter by evaluating the inverse Fourier transform of HD(ω)
Select a suitable window function w[n] based on the specifications
The values of the actual FIR coefficients, h[n] are obtained by :
h[n] = hD[n]w[n]

## Slide 29: 5.2 Design Example
Using the window method, obtain the coefficients of an FIR low-pass filter to meet the specifications below:
  passband edge frequency = 1.5 kHz  20 Hz
  passband ripple < 0.05 dB
  transition width ≤ 0.5 kHz
  stopband attenuation > 50 dB
  sampling frequency = 8 kHz

## Slide 30: Design example (cont)
From the table on p.26, it is known that both the Hamming and Blackman window will satisfy the stopband attenuation requirement
For simplicity, the Hamming window is used
  F = 0.5/8 = 0.0625;
  2M = 3.3 / F = 52.8 ⇒ M is selected as 26
  pTs = 21500/8000 = 2(0.1875)

## Slide 31: Design example (cont)
The ideal low-pass filter coefficients :
The Hamming window coefficients :

## Slide 32: Design example (cont)
The final FIR filter
Note that the filter is non-causal, i.e. having coefficients at negative time
Need to shift by 26 samples such that h[n] starts at n = 0
From the shift property of the Fourier transform, shifting h[n] will only add a phase shift to H(ω) but will not change its magnitude

## Slide 33: Design example (cont)
The resulting FIR filter and its FFT (zero-padded to 512 points):
Shifted 26 samples
0Hz
8000Hz
1500Hz

## Slide 34: Design example (cont)
1.0019
0.9981
p = passband deviation
= 0.0019  20log(1+0.0019) ≈ 0.016 dB (Spec: < 0.05 dB)

fp = 80/512*8000 Hz
= 1250 Hz (Spec: 1500 Hz)


## Slide 35: Design example (cont)
Transition width
= fs - fp
= 520 Hz (Spec: < 500 Hz)
0.0025
s = stopband deviation
= 0.0025  20log(0.0025)
≈ -52 dB
Stopband attenuation = -20log(s/(1- p)
≈ 52 dB (Spec: >50 dB)

fs = 113.3/512*8000 Hz
= 1770 Hz


## Slide 36: Design example (cont)
Two specifications cannot be met
Reason 1: Approximation made in M – lead to error in transition width
Reason 2: fp of HD(ω) is not the fp of HT(ω)
For Hamming window,
fp of HD(ω) always locates at the middle of the transition band

## Slide 37: Design example (cont)
Approximate 3.3 / F as the next even number larger than 3.3 / F , i.e. 54 in this case. Hence, M can be set as 54/2 = 27
fp(ideal) of HD(ω) can be set as
fp (ideal) = fp + (transition width) / 2
For this example,
fp (ideal) = 1500 + 500 / 2
= 1750 Hz

## Slide 38: Design example (cont)
0.9981
1.0019
fp = 97/512*8000 Hz
= 1515 Hz (Spec: 1500 Hz  20 Hz)
M = 27

p = passband deviation
= 0.0019  20log(1+0.0019) ≈ 0.016 dB (Spec: < 0.05 dB)


## Slide 39: Design example (cont)
fs = 128.8/512*8000 Hz
= 2012 Hz
Transition width
= fs - fp
= 2012 – 1515
= 497 Hz

Stopband attenuation = -20log(s/(1- p)
≈ 52 dB (Spec: >50 dB)


## Slide 40: 5.3 Designing high-pass and band-pass FIR filters
The procedure of designing a high-pass FIR filter is nearly the same as for low-pass filters
The only difference – starting with an ideal high-pass filter:
  Specify the desired ideal high-pass frequency response, HHPD(ω)
  Obtain the impulse response, hHPD[n], of the desired filter by evaluating the inverse Fourier transform of HHPD(ω)
  Select a suitable window function w[n] based on the specifications
  The values of the actual FIR coefficients, h[n] are obtained by : hHP[n] = hHPD[n]w[n]

## Slide 41: From low-pass to high-pass
An ideal high-pass filter can be designed from an ideal low-pass filter
Given that an ideal low-pass filter having a magnitude response HLPD() and the passband frequency at fp. The magnitude response of an ideal high-pass filter HHPD() having the same passband frequency can be obtained by
  
  
1

## Slide 42: Impulse response of ideal high-pass filter
n
1
0

## Slide 43: Designing band-pass FIR filters
A band-pass filter has two transition bands – one on the lower frequency side and one on the higher frequency side
If both transition bands have the same specifications, a band-pass FIR filter can be designed using the same approach, but starting with an ideal band-pass filter
  Specify the desired ideal band-pass frequency response, HBPD(ω)
  Obtain the impulse response, hBPD[n], of the desired filter by evaluating the inverse Fourier transform of HBPD(ω)
  Select a suitable window function w[n] based on the specifications
  The values of the actual FIR coefficients, h[n] are obtained by : hBP[n] = hBPD[n]w[n]

## Slide 44: From low pass to band pass
An ideal band-pass filter can be constructed from two ideal low-pass filters
  
(frequency)
1
  
  
(frequency)
1
  
  
1
  
=
(frequency)
-

## Slide 45: Impulse response of ideal band-pass filter

## Slide 46: Limitations of the windowing method
This method is applicable only when HD() can be put into a closed form mathematical expression
  Hence we can derive hD[n] using the inverse Fourier transform
  If not, a different approach, namely the frequency sampling method, should be used
    Numerically compute the inverse discrete Fourier transform of a sampled HD()
The use of windows offers very little design flexibility
  Ripples of passband and stopband must be the same
  Passband frequency of HD() must be at the middle of the transition band
    No way to clearly specify the final passband and stopband frequency
  No way to clearly specify the transition width of H() in the design

## Slide 47: Limitations of the windowing method (cont)
Need human effort to manually adjust the design for achieving the specifications
  Current approaches add an automatic optimization method to search for the best design parameters – the optimal method

## Slide 48: 5.4 Linear Phase Response and Its Implications
The ability to have an exactly linear phase response is one of the most important properties of FIR filters
A filter with linear phase response can maintain the phase relationship of a signal consisting of several frequency components
After processed by the filter, the signal may be delayed but not distorted (in phase and amplitude)
The transfer function of an LTI system H() can be expressed in terms of its magnitude and phase response
A filter is said to be linear phase if its phase response, (), satisfies one of the following conditions:
 (Ts) = -Ts
or  (Ts) = - Ts where  and are any real nos

## Slide 49: Linear phase response
Assume a signal x[n] has two components x1[n] and x2[n]
Assume a filter h1[n] has a unit magnitude response, i.e. |H1(Ts)| = 1, and linear phase response, e.g. 1 (Ts) = -2Ts, thus
Both components will have the same delay, hence no distortion

## Slide 50
Effect of linear phase: E.g.

## Slide 51
Effect of linear phase: E.g.
Output is delayed but not distorted

## Slide 52: Non-linear phase response
Now, assume another filter h2[n] which also has a unit magnitude response, i.e. |H2(Ts)| = 1, but a non-linear phase response, e.g.
 2(Ts) = −(150/π)(ωTs)2 + 3 ωTs,
hence

## Slide 53
Effect of non-linear phase: E.g.
Different delays to different frequencies: output distorted

## Slide 54: Conditions for Linear Phase
The necessary and sufficient condition for an FIR filter to have a linear phase response is that its impulse response, h[n], must be symmetrical or anti-symmetrical.
Also desirable that the filter should have real (not complex numbers) coefficients h[n] in time domain
That is
h[n] = h[N-1-n] or
h[n] = -h[N-1-n]
where N is the length of the filter

## Slide 55: Example
Consider a symmetrical filter with N = 7
We have h[0] = h[6]
h[1] = h[5]
h[2] = h[4]
h[3]
Note that all h[n] are real number
The Fourier Transform of the filter becomes
1
2
4
5
6
3

## Slide 56: Example (cont)

## Slide 57: Example (cont)
A(Ts)
The term A(Ts) are real numbers (not imaginary) but can be positive or negative
We may consider
Then the phase is
which are both linear phase according to our definition

## Slide 58: Four types of linear phase filters
There are four types of linear phase filters, as illustrated in the following examples
2
4
6
8
10
12
0
n
1
3
5
7
9
11
1
N = 13 (odd)
Centre of symmetry
(N odd, positive symmetry)
2
4
6
8
10
0
n
3
5
7
9
1
11
N = 12 (even)
Centre of symmetry
(N even, positive symmetry)
2
4
6
8
0
n
3
5
7
1
N = 9 (odd)
Centre of symmetry
(N odd, negative symmetry)
2
4
6
8
0
n
3
5
7
1
9
N = 10 (even)
Centre of symmetry
(N even, negative symmetry)