## Slide 1: fourier Analysis – theory and implementation
Chapter 2
References:
J. H. McClellan, R. W. Schafer and M. A. Yoder, Signal Processing First, Pearson Education, Inc. 2003, Chapter 3, 4 and 13.
S. K. Mitra, Digital Signal Processing – A Computer-Based Approach, McGraw-Hill International Edition, 4th Ed., 2011, Chapter 3, 5 and 11.

## Slide 2: 2.1 Fourier analysis
We are interested in signal representation in the frequency domain (or the spectrum) since it can give us information that sometimes cannot be seen in the time domain
Signals in the frequency domain can usually be obtained by making use of the Fourier Analysis
Many applications:
  Equalizer for audio signals
  Frequency division multiplexing for communications
  Image and video compression
  Speech and image enhancement
  etc.

## Slide 3: Fourier series
Fourier first showed that any periodic waveform can be synthesized by a sum of sinusoids that are harmonically related
Periodic signal:
Signals that repeat itself within a fixed period

## Slide 4: Fourier series
Harmonically related sinusoids:
Sinusoids with frequencies that are multiple of a fundamental frequency
fo = 100Hz (fundamental
frequency or 1st harmonic)
f = 200Hz = 2*fo (2nd harmonic)
f = 300Hz = 3*fo (3rd harmonic)
f = 500Hz = 5*fo (5th harmonic)

## Slide 5: Fourier series
Any continuous-time periodic waveform can be represented by the Fourier series as follows:
An infinite series
Summation operator: Take the sum of the following function for k = 1, 2, …, 
The bias of x or dc of x (dc here stands for signals that will not change in time, just like direct current in electric circuit, as opposed to alternating current (ac))

## Slide 6: Phasor representation of Fourier series
Recall Euler’s theorem
Hence
We can rewrite Fourier series in the phasor form
+…
Or
where ,
See the proof in Appendix A

## Slide 7: Fourier series
{Xo, X1, X2, …, X} are the Fourier series coefficients
Each coefficient controls the amplitude of the corresponding harmonic required to construct a signal
Some signals need less harmonics, some signals need more
For example, to 100% synthesize a square wave, basically need infinite number of harmonics
The fact is even if you have  number of harmonics, you still cannot obtain a 100% square wave. It is due to the Gibbs phenomenon

## Slide 8
Gibbs phenomenon

## Slide 9: Fourier series analysis
Given a periodic signal, how do we know its Fourier series coefficients Xk?
By Fourier series analysis,
where
See the proof in Appendix B

## Slide 10: Frequency response
The Fourier series coefficients are also referred to as the frequency response (or spectrum) of a periodic signal
T0/2
-T0/2
T0
Assume f0 = 1/T0 = 25Hz
i.e., magnitude of the fundamental freq. (25Hz)
i.e., magnitude of 2nd harmonic (50Hz)
(40 msec)

## Slide 11: 2.2 The Fourier transform
Fourier series analysis helps us to find the spectrum of periodic signals
Most signals are not periodic
  Speech, audio, etc.
Need another tool to find the spectrum of non-periodic (aperiodic) signals
 The Fourier Transform

## Slide 12: The Fourier transform of continuous-time signals
Let x(t) be an aperiodic continuous-time signal, the spectrum of x(t) is given by the Fourier transform as follows:
Or if we know the spectrum X(), we can reconstruct the signal by means of the inverse Fourier transform :
No longer discrete, it is continuous in frequency domain
Frequency, now any real number

## Slide 13: Spectrum of aperiodic signals
x(t)
X()
t
0
-B 0 B

Time Domain
Frequency Domain
X[k]
-B 0 B
k
Periodic
Aperiodic
x(t)
t
0
Fourier series
Fourier transform
Discrete
Continuous

## Slide 14: The Fourier transform of discrete-time signals
Let x(t) be an aperiodic continuous-time signal, x[n] is the samples of x(t) such that:
The spectrum of x[n] is given by the Fourier transform as follows:
x[n] = x(nTs)
or
Normalized radian frequency

## Slide 15: Periodic spectrum of discrete-time signals
It is interesting to note that discrete aperiodic signals have periodic spectrum
It is because
1

## Slide 16: Periodic spectrum of discrete-time signals
0
2
-2

## Slide 17: Relationship with the spectrum of continuous-time signals
If x(t) has a spectrum of X() and x[n] = x(nTs) has a spectrum of Xp(Ts), it can be shown that

## Slide 18: The Fourier transform
Ideal low pass filter
x(t)
X()
t
0
-B 0 B

1
x[n] = x(nTs)
n
-2/Ts 0 2/Ts
Time Domain
Frequency Domain
We can always get back the original continuous signal from the sampled signal by using an ideal low pass frequency filter

## Slide 19
n
Time Domain
Frequency Domain
1
t
0
-B 0 B

0 | |Ts
-2 /Ts 0 2/Ts
-2/Ts 0 2/Ts
x(t)
X()
x[n]
n
x[n]
0 | |Ts
See the aliasing effect of reducing the sampling rate

## Slide 20
Time Domain
Frequency Domain
1
t
0
-B 0 B

-2/Ts 0 2/Ts
x(t)
X()
n
x[n]
0 | |Ts
See the aliasing effect of reducing the sampling rate
x’(t)
t
0
-B 0 B

X’()

## Slide 21: Shannon sampling theorem
Given that a real signal is sampled at frequency . If the signal has frequency components beyond /Ts, after sampling, these frequency components will affect the other replicas in the spectrum
Even with an ideal low pass filter, the original signal cannot be reconstructed. This is the so-called alias effect
Restate the Shannon Sampling Theorem for general aperiodic signals. If a real signal is sampled at frequency and the maximum frequency component of the signal is at frequency , then

## Slide 22: Shannon sampling theorem
A continuous-time real aperiodic signal x(t) with frequencies no higher than fmax can be reconstructed exactly from its samples x[n] = x(nTs) if the samples are taken at a rate fs = 1/Ts that is greater than 2fmax
Nyquist Rate

## Slide 23: Real example
Time Domain
Frequency Domain
Ideal low pass filter and inverse Fourier transform
Resulted signal

## Slide 24: Real example
Time Domain
Frequency Domain
Ideal low pass filter and inverse Fourier transform
Resulted signal

## Slide 25: Real example
Time Domain
Frequency Domain
Ideal low pass filter and inverse Fourier transform
Resulted signal

## Slide 26: How to solve the aliasing problem?
Increase the sampling rate such that fs  2fmax
Use anti-aliasing filter first
Pre-filter the input signal such that it will never has frequency components beyond
Pre-filter
A/D
Digital Signal Processor
D/A
Post-filter

## Slide 27
n
Time Domain
Frequency Domain
1
t
0
-B 0 B

0 | |Ts
-2/Ts 0 2/Ts
x(t)
X()
x[n]
Anti-aliasing
filter
1
X()
-/Ts 0 /Ts

## Slide 28
Ideal low pass filter
Ideal low pass filter
With anti-aliasing filter
Without anti-aliasing filter

X’()
X’()

Look better

## Slide 29: Hear the effect
Original
44.1kHz
sampling
8kHz
sampling
with aliasing
8kHz
sampling
with anti-aliasing filter

## Slide 30: 2.3 Discrete Fourier transform
Spectrum of aperiodic discrete-time signals is periodic and continuous
Difficult to be handled by computer
Since the spectrum is periodic, there’s no point to keep all periods – one period is enough
Computer cannot handle continuous data, we can only keep some samples of the spectrum
Interesting enough, such requirements lead to a very simple way to find the spectrum of signals
 Discrete Fourier Transform

## Slide 31: Discrete Fourier transform
Recall the Fourier transform of an aperiodic discrete sequence
Assume x[n] is an aperiodic sequence with N samples, i.e. {x[n] : n = 0,1, ..., N-1}

## Slide 32: Discrete Fourier transform
If we are now interested only in N equally spaced frequencies of 1 period of the Fourier spectrum, i.e.
0
2
-2
If N = 13
k = 0
k = 4
2/N

## Slide 33: Discrete Fourier transform
Now if we want to compute the value of these N frequencies,
Discrete Fourier Transform
for k = 0,1,…, N-1

## Slide 34: Discrete Fourier transform
Discrete Fourier Transform (DFT) is exactly the output of the Fourier Transform of an aperiodic sequence at some particular frequencies
1
Inherently DFT is periodic since X[k+N] = X[k], although we always only consider one period of X[k]

## Slide 35: Inverse DFT
If we know X[k], we can reconstruct back the signal x[n] via the inverse discrete Fourier transform
for n = 0,1,…, N-1
Inverse Discrete Fourier Transform

## Slide 36: Inverse DFT
It can be proven as follows:
See the proof in Appendix C

## Slide 37: Frequency representation of DFT
The DFT of a data sequence is another data sequence . What is the frequency represented by each component of ?
0
2
-2
If N = 13
k = 0
k = 4

## Slide 38: Frequency resolution of DFT
Although DFT gives exact frequency response of a signal, sometimes it may not give the desired spectrum
0
n
9
N = 10
x[n]
One period of
k
10
X[k] if N = 10
So different from
Fourier
Transform
DFT

## Slide 39: Frequency resolution of DFT
Need improved resolution
Achieve by padding zeros to the end of x[n] to make N bigger
0
n
50
x[n]
9
x[n] = {1 1 1 1 1 1 1 1 1 1 0 0 0 0 … 0}
40 zeros
Pad 40 zeros
49

## Slide 40: Frequency resolution of DFT
The Fourier transform of a signal will not change if we pad zeros to the end of it
Given the Fourier Transform of is , i.e.
Let has a length of samples, then
0

## Slide 41: DFT of zero padded sequence
N = 50

## Slide 42: DFT of zero padded sequence
N = 100

## Slide 43: Summary
Periodic signal
Fourier Series
Analysis
Discrete spectrum

## Slide 44: Summary
Non-Periodic continuous
signal
Fourier
transform
Continuous spectrum
0

## Slide 45: Summary
Non-Periodic discrete
signal
Fourier
transform
Continuous periodic
spectrum
0
-2
2

## Slide 46: Summary
Non-Periodic discrete
signal
Discrete Fourier
transform
Determine only N samples of one period of the Continuous periodic spectrum
0
-2
2

## Slide 47: Properties of DFT
Recall the formulation of DFT,
Linear property
  If X1[k] is the DFT of x1[n] and X2[k] is the DFT of x2[n], then

## Slide 48: Properties of DFT
Circulant property (periodicity):
  If X[k] is the DFT of x[n] with N samples,
Shift property:
  Given that X[k] is the DFT of x[n]. If y[n] is a shifted version of x[n] such that y[n] = x[n-m], then
0
-N
N

## Slide 49: Properties of DFT
Symmetry properties:
  If x[n] is real (none of x[n] contains imaginary number) and if X[k] can be written as
  then
Xr[k]
k
0
N
2N
-N
-2N
Xi(k)
k
0
N
2N
-N
-2N
Odd symmetry
Even symmetry

## Slide 50: Properties of DFT
Symmetry properties:
  If x[n] is real and even symmetry (an even function), i.e. x[n] = x[N-n], then
  If x[n] is real and odd symmetry (an odd function), i.e. x[n] = -x[N-n], and x[0] = x[N/2] = 0 (if N is even), then
and
and

## Slide 51: 2.4 Fast Fourier Transform
A Historical Perspective
  The Cooley and Tukey Fast Fourier Transform (FFT) algorithm is a turning point to the computation of DFT
  Before that, DFT was never practical except running by some very expensive computers
  FFT gives nearly a factor of 1000 improvement in the computation speed over the traditional approach in most computing environments

## Slide 52: Principal discoveries of DFT computation
Researcher(s) Date Feature
Cooley & Tukey 1965 Any 2n composite integer
I.J. Good 1958 Any integer with relatively prime factors
L.H. Thomas 1948 Any integer with relatively prime factors
Danielson 1942 2n
K. Stumpff 1939 2nk, 3nk
C. Runge 1903 2nk
J.D. Everett 1860 12
A. Smith 1846 4, 8, 16, 32
F. Carlini 1828 12
C.F. Gauss 1805 Any composite integer
Fourier proposed Fourier series in 1807 !

## Slide 53: Basic principle
The basic principle of FFT is “divide and conquer”
 To break down a big problem to a number of smaller problems and tackle them individually
Need to satisfy the following criterion

## Slide 54: Basic principle
Big Problem
Smaller
Problem
Smaller
Problem
Smaller
Problems
Overhead
Apply Divide and Conquer iteratively

## Slide 55: Operation of FFT
Length-N/4 DFTs
For each round, the size of the problem is divided by 2
Length-N DFT
Length-N/2
DFT
Length-N/2
DFT
Overhead

## Slide 56: Mathematical Derivation
Recall the DFT of x[n], for n = 0, 1,…,N-1
Separate the summation into two groups
for k = 0, 1,…,N-1
for k = 0, 1,…,N-1

## Slide 57: Example
If DFT of x[n] is
We separate it into two groups with odd and even n

## Slide 58: Mathematical Derivation
for k = 0, 1,…,N-1

## Slide 59: Mathematical Derivation
Since
Length-N/2 DFT of data with even n
Overhead
Length-N/2 DFT of data with odd n
for k = 0, 1,…,N-1
Note that G[k] = G[k+N/2]; H[k] = H[k+N/2]

## Slide 60: Example: N = 8
N/2 = 4 point DFT
x[0]
x[2]
x[4]
x[6]
N/2 = 4 point DFT
x[1]
x[3]
x[5]
x[7]
G[0]
G[1]
G[2]
G[3]
H[0]
H[1]
H[2]
H[3]
X[0]
X[1]
X[2]
X[3]
X[4]
X[5]
X[6]
X[7]
W86
W85
W84
W83
W82
W81
W80
W87

## Slide 61: How much it saves?
Assume x[n] has N data and each data is a complex number
For each k, it needs N complex multiplications and N-1 complex additions
In overall, it needs N2 complex multiplications and N(N-1) complex additions
for k = 0, 1,…,N-1

## Slide 62: How much it saves?
FFT converts an N-point DFT to 2 N/2-points DFTs
for k = 0, 1,…,N-1
(N/2)2 complex multiplications
N/2(N/2-1) complex additions
N complex multiplications

## Slide 63: Computational complexity
262,144x/261,632+
131,584x/131,072+
N
DFT
1-stage FFT
4
16x/12+
12x/8+
8
64x/56+
40x/32+
16
256x/240+
144x/128+
32
1,024x/992+
544x/512+
64
4,096x/4,032+
2,112x/2,048+
128
16,384x/16,256+
8,320x/8,192+
256
65,536x/65,280+
33,024x/32,768+
1024
1,048,576x/1,047,552+
525,312x/524,288+
512

## Slide 64: Computational complexity
Obviously
We can re-apply the same approach to the decomposed N/2 problems

## Slide 65: Example: Apply to G[k] and H[k]
x[0]
x[4]
x[2]
x[6]
x[1]
x[5]
x[3]
x[7]
X[0]
X[1]
X[2]
X[3]
X[4]
X[5]
X[6]
X[7]
W87
W86
W85
W84
W83
W82
W81
W80
N/4 = 2 point DFT
N/4 = 2 point DFT
N/4 = 2 point DFT
N/4 = 2 point DFT
W43
W42
W41
W40
W43
W42
W41
W40

## Slide 66: Further decomposition
The complexity is further reduced
The above decomposition is recursively performed until a length-2 DFT is computed
A length-2 DFT can be implemented as a butterfly as follows:
x[0]
x[1]
X[0]
X[1]

## Slide 67: Final “butterfly” structure
x[0]
x[4]
x[2]
x[6]
x[1]
x[5]
x[3]
x[7]
X[0]
X[1]
X[2]
X[3]
X[4]
X[5]
X[6]
X[7]
W87
W86
W85
W84
W83
W82
W81
W80
W43
W42
W41
W40
W43
W42
W41
W40
-1
-1
-1
-1

## Slide 68: Further simplification
The complexity can be further reduced. For every butterfly, it can be converted as follows:
1
-1
Since

## Slide 69: Further simplified structure
-1
x[0]
x[4]
x[2]
x[6]
x[1]
x[5]
x[3]
x[7]
X[0]
X[1]
X[2]
X[3]
X[4]
X[5]
X[6]
X[7]
W83
W82
W81
W80
-1
-1
-1
-1
-1
-1
-1
-1
-1
-1
-1
W41
W40
W41
W40
FFT
Total complex multiplication: 5
Total complex addition: 24
DFT
Total complex multiplication: 64
Total complex addition: 56
W20
W20
W20
W20

## Slide 70: Relationship between input and output indices
From the length-8 DIT FFT flowgraph, it is seen that the input and output are not in-order
  The input data needs to shuffle before performing the DIT-FFT
The input and output indices of DIT-FFT follow a bit-reversal relationship
For example: Length-8 DIT-FFT
Input: x[0] – 000 => Output: X[0] – 000
x[4] – 100 => X[1] – 001
: ;
x[3] – 011 => X[6] – 110
Also apply to other sequence lengths

## Slide 71: Remarks
FFT of the form above is called decimation-in-time (DIT) FFT (or Cooley and Tukey FFT)
In general, the complexity of DIT FFT is
  (N/2)log2N complex multiplications (W0 is considered as multiplication in this expression)
  Nlog2 N complex additions
DIT FFT requires N to be a power of 2
If N is not a power of 2, need zero padding to let N be a power of 2 before FFT
More than a hundred of FFT algorithms after DIT FFT for different applications

## Slide 72: Appendix A – Proof of the Fourier series in complex number form

## Slide 73: Appendix A – Proof of the Fourier series in complex number form
where
(Q.E.D.)

## Slide 74: Appendix B – Proof of the Fourier series analysis
From Appendix A
Hence

## Slide 75: Appendix B – Proof of the Fourier series analysis
Also from Appendix A
(Q.E.D.)

## Slide 76: Appendix B – Proof of the Fourier series analysis
0
A0
That is,
(Q.E.D.)

## Slide 77: Appendix C – Proof of the formulation in inverse DFT
It is known from the geometric series that,
Hence
So if m  n,
If m = n,
(Q.E.D.)