## Slide 1: EIE4413 Digital Signal Processing
Dr Daniel Lun
Department of Electronic and Information Engineering
The Hong Kong Polytechnic University
Office: DE637 Tel: 27666255
Email: enpklun@polyu.edu.hk
https://staff.eie.polyu.edu.hk/enpklun/
Course material can be found in the Blackboard

## Slide 2: Topics
Introduction
Fourier analysis – theory and implementation
Convolution and implementation
The Z transform and digital filter realization
FIR and IIR filter designs
Statistical signal processing and applications

## Slide 3: Subject learning outcomes
Upon completion of the subject, students will be able to:
  Understand the basic concepts of Fourier analysis of digital signals and apply them to practical problems.
  Design and realize simple digital filters for practical applications.
  Understand the importance of random signal processing in DSP, and its application in statistical measures, prediction and data modelling.
  Design and simulate simple DSP systems.

## Slide 4: Assessment plan
Examination (60%)
Continuous assessment (40%)
  >10 short exercises (in-class exercises) (5%)
  2 assignments (5%): to prepare for the test and exam
  3 lab reports (10%): and 3 demos too
  2 tests (20%)

## Slide 5: References
Textbooks:
S.K. Mitra, Digital Signal Processing, 3rd Edition, McGraw-Hill Education (Asia), 2009.
J.G. Proakis and D.G. Manolakis, Digital Signal Processing: Principles, Algorithms and Applications, 4th Edition, Pearson International Edition, 2007.
E.C. Ifeacher and B.W. Jervis, Digital Signal Processing - A Practical Approach, Prentice Hall (Pearson Education), 2002.
Plus other reference materials given by the subject lecturer

## Slide 6: Introduction
Chapter 1

## Slide 7: Why “Digital Signal Processing”?
What are signals?
  “Something” that carry information
    “Something”  pattern of variations of physical quantity that can be manipulated, stored, or transmitted by physical process
    e.g. Speech signals, audio signals, image signals, video signals, radar signals, etc.
Human beings use different kind of signals to convey information
  They are the basis of all information systems
  Need thorough study of their manipulation, storage, and transmission

## Slide 8: Examples of signals
Speech
Audio
Image
Video
Multimedia

## Slide 9: Why “Processing”?
The original form of signals may not suit the needs of conveying information
  E.g. speech signals
    Volume too low, too noisy, not enough intelligibility, etc.
  E.g. image signals
    Too blur, too dark, not colorful enough, etc.
It is often that we have no way to inform the signal sources to change their signals
Desirable if they can be processed after received

## Slide 10: Why “Digital”?
Signals can change to other physical form, e.g. electricity
wave
change of voltage
mic
Light
Lens
CCD
Object
change of voltage
Facilitate manipulation, storage, and transmission using electrical equipment

## Slide 11: Why “Digital”?
After conversion, many signals become voltage changing with time, e.g. speech
For every time instant, signal is found
Hence continuous-time signal (or analogue signal)
Most natural signals, such as speech, audio, etc. are continuous-time signals
time
voltage

## Slide 12: Why “Digital”?
With the advance of computer technology, we want to process signals by computer
Computer can only handle data, but not continuous signals
Need sampling
   extract signal at some time instants
   Discrete-time signals
time
voltage
Signal is found only at some instants
Discrete-time signal
2v
4v
4.2v

## Slide 13: Why “Digital”?
Moreover, computers only understand and
  Discrete-time signal at every instant needs to be converted into “digital” data
  Need Analogue/Digital (A/D) converter
After processing, digital data needs to be converted back to analogue continuous-time signal
  Need Digital/Analogue (D/A) converter and
  Low pass filter (why?)

## Slide 14: Typical DSP system
Mic
Sound card with sampler
(or A/D converter)
Processed signal
D/A converter and low pass filter
speaker

## Slide 15: Then why NOT analogue signal processing?
DSP has a few important advantages over directly processing analogue signals
  Perfect reproducibility
    No drift in performance with temperature or age
  Suitable for VLSI implementation
    VLSI favors digital systems
  Greater flexibility
    DSP systems can be programmed and reprogrammed to perform a variety of functions, without modifying the hardware
  Superior performance
    New methods are found for processing signals in discrete domain but hardly in analogue domain

## Slide 16: Typical steps to construct a DSP system
Prepare all the required hardware
  Generate digital data for processing at the computer input
  Convert digital data from the computer output to analogue signal
Develop signal processing algorithm
  Express input and output in mathematical form
  Using mathematics to figure out the solution to the problem
Realize the signal processing algorithm
  Translate the algorithm into computer program
  Execute the program with the computer
Input
Output

## Slide 17: Example – To amplify a signal
Start with an analogue signal x(t) …
x(t)
x: a symbol represents this signal
t: a real number variable
x(t) is defined for all value of t, hence continuous
e.g. x(0) = 0; x(70.5) = -90.5; x(100.23) = 80
t = 100.23
t = 70.5
t = 0
We use () to indicate that x is continuous

## Slide 18: Example – To amplify a signal
We use [] to indicate that x is discrete
The sampler converts x(t) to become a discrete-time signal x[n]
x[n]
x: a symbol represents this signal
n = 0
n = 100
n = 70
x[n] is defined only at some instants of time, since n is integer
e.g. x[0] = 0; x[70] = -90.5; x[100] = 80
n: an integer variable

## Slide 19: Example – To amplify a signal
Ts – Sampling period
x(t)
x[n]
x[n] = x(nTs)
x[0] = x(0)
x[1] = x(Ts)
x[2] = x(2Ts)
x[3] = x(3Ts)
: :

## Slide 20: Example – To amplify a signal
Input
(256 samples)
1. Develop signal processing algorithm
  Input – x[n]; Output – y[n]
  y[n] = x[n] × 2 for all n (algorithm)
2. Realize the signal processing algorithm
  main()
  { int n, x[256], y[256]; x = zeros(1,256);
  for (n=0; n<256; n++) y = zeros(1,256);
  // Get data and store in x % Get data and store in x
  y[n] = x[n]*2; y = x*2;
  }
Output
(256 samples)
Our task: Output = Input x 2
C Program
Matlab Program

## Slide 21: Summary
Digital signal processing has many advantages over directly processing a signal in analogue form
Digital signal processing needs special hardware such as sampler, A/D, D/A converter and low pass filter for its implementation
Mathematic derivation and programming are equally important when constructing a DSP system

## Slide 22: Summary
All of the above are based on an important theorem, namely the Shannon sampling theorem,
  Analogue signals can be reconstructed from their discrete-time counterpart without significant error if certain criteria are fulfilled
To understand the Shannon sampling theorem, we need to first understand the frequency response of signals